## Slide 1: Introduction to Raspberry Pi
Rochester MakerSpace
2019

## Slide 2: Raspberry Pi 3 B+
Broadcom BCM2837B0, Cortex-A53 (ARMv8) 64-bit SoC @ 1.4GHz
1GB LPDDR2 SDRAM
2.4GHz and 5GHz IEEE 802.11.b/g/n/ac wireless LAN, Bluetooth 4.2, BLE
Gigabit Ethernet over USB 2.0 (maximum throughput 300 Mbps)
Extended 40-pin GPIO header
Full-size HDMI
4 USB 2.0 ports
CSI camera port for connecting a Raspberry Pi camera
DSI display port for connecting a Raspberry Pi touchscreen display
4-pole stereo output and composite video port
Micro SD port for loading your operating system and storing data
5V/2.5A DC power input

## Slide 3: History
The Raspberry Pi was created in February 2012 by the Raspberry Pi Foundation to promote and teach basic computer science in schools and colleges around the UK.
The Raspberry Pi Foundation is a UK-based charity that works to put the power of computing and digital making into the hands of people all over the world. We do this so that more people are able to harness the power of computing and digital technologies for work, to solve problems that matter to them, and to express themselves creatively.
More than 1M units sold in the first year, more than 4.5M by 2014

## Slide 4: Linux with GPIO!
At 1.4MHz, quad-core and 1MB of RAM, RPi is a capable small Linux system
GPIO adds possibility of creating different projects e.g., robots

## Slide 5: Comparison vs. Arduino
Pros
  More RAM + Storage
  More processing power
  Debug in place
  Multiple, concurrent programs
  Built-in HDMI and camera interfaces
  Built-in WiFi and Bluetooth comms
  Built-in Ethernet and 4 USB ports
  Pluggable SD card to expand memory
Cons
  Non-real-time OS makes real-time programming impractical
  Requires some understanding of Linux
  Much more configuration required
  More electrical power required
  No A/D inputs
  Narrow input voltage tolerance
Bottom Line: Choose the right tool for the job

## Slide 6: Next Steps
Check out these sources of information
  Raspberry Pi Manual
  Raspberrypi.org
  www.elinux.org
  Adafruit.com/category/105 – Raspberry Pi products and accessories
  Youtube.com
Design a project or program and get started!
  Lots of examples online if you are looking for inspiration